Revision Notes

# Electron Devices

### Electron Drift Velocity

Where mu-sub-n is the mobility of electrons (defined for the material) and epsilon is the electric field.

### Contact Potential Equation:

Where V0 is contact potential

kT/q is 25mV (at 300K)

Na is concentration of acceptors (holes) on p-side

Nd is concentration of donors (electrons) on n-side

ni is the intrinsic carrier concentration.

### Fermi-Dirac Distribution function (first term’s work)

### Diode Equation

### Diode Capacitance

Junction capacitance, where W is the width of the depletion/transition region and epsilon is the permittivity.

This is dominant during reverse bias.

Storage capacitance, varies with forward bias voltage. Normally dominant in forward bias, and used in voltage-variable capacitors (varicap diodes).

# Communications (Tim Tozer)

### LCR parallel circuit:

### Amplitude Modulation

e = modulated signal

m = modulation index (between 0 and 1, usually 0.3)

### Nyquist’s sampling theorem

Sampling frequency = 2 x maximum frequency

### Quantisation noise power

Delta-v is the step size.

### Thermal noise power

N= noise power in watts

k = Boltzmann’s Constant = 1.38 x 10-23 J/K = -229 dB J/K

T = noise temperature in Kelvin

B = bandwidth in Hz

This equation does assume a precisely matched load.

# Maths (Ken Todd- term 2)

### Total Differential

Where z is a function of x and y and x and y are functions of t.

### Change of Variables

If z is a function of x and y, and x and y are both functions of u and v, then:

And, similarly

### Taylor’s Series in two variables

### Stephenson’s method

Treat h and k as constants, to get the series in terms of h and k

Substitute h and k for a,b,x & y.

### Finding Stationary points

At a stationary point:

To check for a saddlepoint, use the Del operator:

If (>0 then you have a saddlepoint. Otherwise, check the partials for a maximum or minimum.

### Double Integrals

A Double Integral is the volume under a surface, as defined by four limits.

Static Fields

## Electrostatics:

### Coulomb’s Law

### Electric Field due to a point charge

### Electric Field due to a line charge

Rho is charge density in Cm-1

### Electric Field due to an infinite sheet of charge

Rho is charge density in Cm-2

### P.D. between two points

Where E is electric field strength and d is distance

### Capacitance of two sheets

where A is the area of the sheets and d is their separation.

### Energy stored in a capacitor:

### Electric Flux Density:

### Displacement current density:

### Conduction current density:

### Generalised form of Ohm’s law:

where sigma is conductivity.

## Magnetic fields:

### Biot-Savart Law:

### Faraday’s Law:

## Inductors

Total flux in an inductor (in Webers)

where k is a geometric constant.

### Voltage induced in inductor:

Self-inductance (in Henrys)

# Transistors

Diode equation (approximate form)

### Small-signal diode resistance

ID is the DC bias current.

### Transistor large-signal behaviour:

### Transistor small-signal behaviour:

## Common-emitter amplifier:

### Voltage gain

### Input resistance

### Output resistance

### Overall gain of CE amplifier with source and load resistance:

## Common-collector amplifier

Voltage gain (just less than unity)

Input resistance (very high)

Output resistance (very low)

Bear in mind that, in a CC amplifier, changing the load resistance changes the input resistance of the amplifier. Changing the source resistance changes the output resistance.

### Common-base amplifier:

Very low input impedance and moderate output impedance

Amplifier characteristic summary (ignoring source and load resistances):

| Configuration | Voltage gain | Current gain | Input resistance | Output resistance |
| --- | --- | --- | --- | --- |
|  | Av | AI | rin | rout |
| CE | -gmRC | ( | r( // RBias | RC |
| CC | (1 | ( | ((re+RE) // RBias | (re |
| CB | gmRC | (1 | (re | RC |

## Onset of clipping in single transistor amplifiers

### For CE and CB amplifiers:

Clipping on the positive half-cycle occurs when the device switches off completely and the voltage across RC is reduced to zero.

Clipping on the negative half-cycle occurs when VCE is less than 0.7V and the transistor saturates.

To get maximum output swing, bias should make VC halfway between VB and VCC.

### For CC amplifiers:

The output always clips first on the negative half-cycle. Distortion occurs when the bias current is equal to the current into RE // RL

The bias current must be large enough to handle the largest desired voltage swing.

## Miller’s Effect

This limits the high-frequency behaviour of transistor amplifiers.

Effective capacitance of transistor:

High-frequency cut-off point (-3dB point):

## Myles’s Transistor Amplifier design guidelines:

Maximum gain from a single-stage amplifier (split-supply):

Load impedance: if then you need a CC output stage

Source impedance: if  where IE is in mA, then use a CC input stage.

## Field Effect Transistors

FETs are transconductance devices- the gate voltage controls the source-drain current.

MOSFETs (Metal-oxide-semiconductor field effect transistors) come in two types, each of which comes in two polarities:

N-channel MOSFETs conduct solely by electrons.

P-channel MOSFETs (less common) conduct solely by holes.

Enhancement-mode MOSFETs have no built-in channel. The channel is induced by the presence of a positive gate voltage. The threshold voltage VT is positive. With no gate voltage, the device is switched off (normally-off).

Depletion-mode MOSFETs are the reverse. The channel is built into the silicon and is controlled by the presence of a negative gate voltage. The threshold voltage is negative. With no gate voltage, the device is switched on (normally-on). To turn the device off, apply a negative gate voltage.

### MOS Capacitors

Assuming p-type silicon substrate:

Making the metal negative relative to the silicon causes accumulation:

Holes are attracted to region under gate

Bands in silicon bend closer to valence band (gets more p-type)

Making the metal positive relative to the silicon causes depletion

Holes at surface of semiconductor are repelled, causing a depletion region to form.

Bands in silicon bend closer to conduction band (gets less p-type)

Making the metal more postive causes inversion:

Energy bands bend further down

Eventually the bands bend enough to make the surface appear locally n-type.

Strong inversion occurs when the surface is as n-type as the bulk is p-type.

When strong inversion occurs, the device has enough charge carriers to conduct usefully. This point is termed the threshold voltage (VT)

## MOS FET DC behaviour

### Drain Current

Where:

ID is the drain current

( is the device constant (or gain constant), normally specified in questions.

VGS is the gate-source voltage

VT is the threshold voltage (normally defined by manufacturer).

VDS is the drain-source voltage.

W is the channel width

L is the channel length (source-drain distance)

( is the mobility

C is the gate capacitance (varies with oxide thickness)

### Drain Current at saturation

This is the region used for small-signal amplifiers.

## MOS FET small-signal AC behaviour

### Small signal transconductance

This equation holds when the device is saturated i.e. VDS>VGS-VT

When biasing FETs, remember that the gate current is zero.

## Common-source amplifier

Used as a gain stage where very high input impedance is required. Frequently used as differential input stages in opamps.

### Small-signal gain:

### Input impedance:

RG may be one resistor (depletion-mode) or two in parallel (enhancement mode)

### Output impedance:

## Common-drain amplifier

Used as a voltage buffer. Near unity gain with very high input impedance and very low output impedance. Usually found at input stages to instrumentation (voltmeters, scopes)

### Small-signal gain:

### Input impedance:

### Output impedance:

## Common-gate amplifier

Gain stage with low input impedance- usually used for video or RF systems requiring 50 or 75 ohm input impedance. Also used as current amplifiers.

### Small-signal gain:

### Input impedance:

### Output impedance:

## NMOS Logic circuits

### NMOS inverter threshold equation

Zpu is the aspect ratio (length-to-width ratio) of the pull-up device.

Zpd is the aspect ratio of the pull-down device.

VTd is the threshold voltage of the depletion mode device (pull-up)

VTe is the threshold voltage of the enhancement mode device (pull-down)

Vinv is the cross-over voltage of the inverter (the point at which it changes state).

The equation gives the ratio of the aspect ratios of the devices.

# Transmission Lines

### Velocity of wave on line

### Characteristic impedance

### Voltage Reflection coefficient

### Voltage Transmission coefficient

### Standing waves:

If you have sinusoidal excitation and (v = 1, then the result is a standing wave:

## Reactive behaviour of mismatched transmission line:

### Short-circuited line of length l:

Infinite reactance occurs when  (quarter-wave system)

Zero reactance (short circuit) occurs when (half-wave system)

### Input impedance of a Tx line with arbitrary termination:

If (half wavelength) then Zin = ZL, so if the tx line is an integer number of half-wavelengths then Zin is independent of Z0.

If (quarter wavelength) then

Rearranging:

This is used for quarter-wave impedance matching: a quarter-wave length of transmission line of a specified characteristic impedance can act as a matching piece:

If you have a 50( source and a 100( load, then . Thus a quarter-wave length of transmission line of 72( will match a 50( system to a 100( system, at the specified frequency.

# Transmission Lines & Static Fields (term 3)

### Gauss’s Law:

This boils down to the fact that the total field radiated by a number of point charges inside an enclosing surface is equal to the sum of all the charges enclosed divided by the permittivity.

### Ampère’s Law

A number of currents are surrounded by a loop. The total magnetic field on the whole loop is equal to the total current passing through it.

## Field Analysis of Coaxial cables

### Capacitance per unit length

b is the radius of the cable outer.

a is the radius of the cable inner.

( is the permittivity of the dielectric.

### Inductance per unit length

### Propagation Velocity

### Characteristic Impedance

### Intrinsic impedance

This is the ratio of electric to magnetic fields in the cable:

## Field Analysis of Parallel Plate Transmission Line

### Capacitance per unit length

w is the width of the plates

d is the plate separation

( is the permittivity of the dielectric.

### Inductance per unit length

### Propagation Velocity

### Characteristic Impedance

## Circuits

## LC Resonant circuits

### Resonant frequency

### Q-factor (Series LC)

### Q-factor (Parallel LC)

## Real, Reactive and Apparent Power

### Apparent Power

Apparent Power is measured in Volt-Amps (VA)

### Real Power

### Reactive Power